## Slide 1
Sustainable energy and the impact on the environment over long time scales, solutions and handling waste from EDF’s perspective. Bath University ISEE seminar 31 October 2017 Humphrey Cadoux-Hudson Managing Director Nuclear Development

## Slide 2: The UK’s leading generator and supplier of electricity
2
1
34
1
7
2
  Meeting around one-fifth of the country’s demand and supplying millions of customers and businesses with electricity and gas.
We generate electricity with eight nuclear power stations, more than 30 wind farms, one gas and two coal power stations.
Leading the UK's nuclear renaissance with the construction of a new nuclear power station at Hinkley Point C.
The leading supplier of electricity to UK businesses.
1
2
PRESSURISED WATER REACTOR
Commissioned 1995
Lifetime expectation 2035+
AGR NUCLEAR STATIONS
14 Advanced gas-cooled reactors
Commissioned 1976-1988
Lifetime expected mid 2020s to 2030
COAL-FIRED STATIONS
Commissioned 1967-1969
Lifetime ambition 2020+
Co-fires biomass at Cottam
GAS STATION (CCGT)
Commissioned 2013
Lifetime 2040+
WIND FARMS
Total operated capacity of ~696 MW
EDF Energy is JV partner with EDF Energy Nouvelles
GAS STORAGE SITES
7 converted salt cavities
Fast injection/withdrawal – up to 7Mtherms/day
PLANNED NEW NUCLEAR STATIONS
Sizewell C
Bradwell B
NUCLEAR STATION UNDER CONSTRUCTION
Hinkley Point C – construction underway
Providing gas and electricity for more than 5 million customer accounts.

## Slide 3
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr
Sales | 5 | 5 | 5
Chart: 
Volume
Capacity flexibility
Sustainability

## Slide 4: Electricity Supply – why we need a managed market to be sustainable
Normal
Commodity Demand = Supply Overtime Volume achieved by international marginal cost of
production and normal economics transport/storage
Electricity
Demand = Supply by micro second Capacity to meet maximum demand in cold winter/hot summer and need to meet changing demand /supply
                Transfer (transmission) is very expensive
                Storage is inefficient /expensive
                Supply needs to be ≥ demand 100% time
                Short term power market = marginal cost of production
                Low carbon will see the power market trend down
Hence a market price will despatch lowest cost generation but not supply adequate reliability for an
advanced economy
Notes: 2 – leave blank for now, I will need to find this chart

## Slide 5: Electricity is fundamental to our economy…
Chart: 
Electricity | 0.014897
 | 0.9851
Real estate | 0.12969
Retail | 0.10953
Manufacturing | 0.097716
Health & social work | 0.078449
Science & technology | 0.074853
Finance & insurance | 0.072225
IT | 0.065097
Construction | 0.061174
Education | 0.058826
Other | 0.23577
Electricity costs <1%
Cost of electricity to society
But ~98% of the economy is reliant on electricity
% of UK GVA (2015p)
Value of electricity to society

## Slide 6: ...but electricity is challenging to manage… supply and demand has to be balanced each second and the system has to be resilient to faults.
There is a minimum demand set overnight in summer by the need for lighting, 24-hour telecommunications and manufacturing [TBC].
And a maximum demand in winter set by the need for heating, cooking and lighting in homes and businesses [TBC].
Hour of day
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Summer (typical day in Jul) | 28.0756 | 27.4466 | 26.4852 | 25.7545 | 24.367 | 24.7406 | 29.6044 | 35.2505 | 38.542 | 40.3624 | 41.1362 | 41.6657 | 41.9056 | 41.0709 | 40.3298 | 39.8429 | 40.6706 | 40.9676 | 39.0958 | 37.4527 | 36.4651 | 36.4378 | 34.9061 | 30.9449
Winter (typical day in Jan) | 38.2141 | 37.4734 | 36.0751 | 34.5295 | 32.2743 | 32.3696 | 37.4509 | 42.8426 | 45.0642 | 47.3393 | 48.3142 | 48.9169 | 49.4045 | 48.7989 | 48.2028 | 47.3706 | 50.8335 | 52.96 | 51.1748 | 49.719 | 47.5077 | 45.1321 | 41.5765 | 38.4232
Final demand, GW
Need for flexible generation or demand to manage hour by hour changes
Customer disconnections threshold
System frequency, Hz
50
The system needs to be resilient to faults to prevent customer disconnections.
Faults include generation disconnections, network failure.
Needs to be managed by a combination of fast-acting response and high capacity units.
System fault leading to rapid change in frequency
Normal operation
Response prevents disconnections
<10 seconds

## Slide 7
Intermittency cost increases with higher levels of decarbonisation
* Marginal intermittency cost represents the incremental system cost incurred by decarbonising with offshore and storage relative to nuclear. System model also includes 20GW solar, 20GW onshore and 11GW interconnection
Chart: Marginal Offshore Intermittency Cost*
| 0.6 | 0.61 | 0.62 | 0.63 | 0.64 | 0.65 | 0.66 | 0.67 | 0.68 | 0.69 | 0.7 | 0.71 | 0.72 | 0.73 | 0.74 | 0.75 | 0.76 | 0.77 | 0.78 | 0.79 | 0.8 | 0.81 | 0.82 | 0.83 | 0.84 | 0.85 | 0.86 | 0.87 | 0.88 | 0.89 | 0.9 | 0.91 | 0.92 | 0.93 | 0.94 | 0.95 | 0.96 | 0.97 | 0.98 | 0.99 | 1
£100/KWh Storage (Today / 4) | 13.8845 | 14.9732 | 16.0901 | 17.2368 | 18.415 | 19.6264 | 20.8728 | 22.1565 | 23.4797 | 24.8449 | 26.2548 | 27.7126 | 29.2215 | 30.7853 | 32.4082 | 34.0947 | 35.85 | 37.6801 | 39.5915 | 41.5919 | 43.6898 | 45.8954 | 48.2203 | 50.6781 | 53.285 | 56.0602 | 59.0269 | 62.2135 | 65.6553 | 69.3968 | 73.4952 | 78.0257 | 83.0903 | 88.8322 | 95.4607 | 103.3005 | 112.8957 | 125.266 | 142.701 | 172.5063
£10/KWh Storage (Today/40) | 14.0409 | 14.3602 | 14.6877 | 15.024 | 15.3695 | 15.7248 | 16.0903 | 16.4667 | 16.8548 | 17.2551 | 17.6686 | 18.0961 | 18.5386 | 18.9972 | 19.4731 | 19.9677 | 20.4824 | 21.0191 | 21.5797 | 22.1663 | 22.7815 | 23.4283 | 24.1101 | 24.8309 | 25.5954 | 26.4092 | 27.2792 | 28.2137 | 29.223 | 30.3202 | 31.5221 | 32.8507 | 34.3359 | 36.0198 | 37.9636 | 40.2627 | 43.0765 | 46.7042 | 51.8171 | 60.5577
1.7TWh storage which represents storage capacity of 185 times the level of Dinorwig pumped storage
(or 170m 10kWh Tesla batteries)
(5.5TWh storage)
54GW Offshore
100g/kWh
50g/kWh
79GW Offshore
Intermittency explained
Intermittency costs reflect costs of backup, spill energy and additional transmission lines
With higher levels of decarbonisation, less and less gas is allowed
Therefore wind has to fill a larger proportion of the demand, even in low-wind periods
This requires either building disproportionate amounts of wind capacity (which is then wasted at times of high wind) or investing in expensive storage solutions

## Slide 8: Our energy mix is changing rapidly
Since 2013 there has been a dramatic decrease in the contribution of coal to our energy mix
This has mostly been replaced by lower carbon gas, increased output from wind, alongside more imports and reduced demand
Nuclear is now the second largest contributor, supplying around 20% of our energy
The Grid is already having to adapt to increasingly variable output from solar and wind
EDF Energy is the UK’s largest electricity generator – operating nuclear, coal, gas and renewables
We are part of this change and are adapting how we operate
Our 4GW of coal stations now only operate during peaks of demand, and we are investing across a range of technologies, including renewables, gas and battery storage
Our investment in the UK’s nuclear power stations has resulted in improved performance and an output that is now 60% higher than a decade ago
Coal is no longer providing the majority of power
Chart: 
| 2011 Q1 | 2011 Q2 | 2011 Q3 | 2011 Q4 | 2012 Q1 | 2012 Q2 | 2012 Q3 | 2012 Q4 | 2013 Q1 | 2013 Q2 | 2013 Q3 | 2013 Q4 | 2014 Q1 | 2014 Q2 | 2014 Q3 | 2014 Q4 | 2015 Q1 | 2015 Q2 | 2015 Q3 | 2015 Q4 | 2016 Q1 | 2016 Q2 | 2016 Q3 | 2016 Q4 | 2017 Q1
Nuclear | 17.668 | 17.3982 | 14.3131 | 13.2759 | 15.6218 | 16.8269 | 16.3776 | 15.1229 | 16.6082 | 14.0517 | 16.974 | 16.4986 | 15.0108 | 15.8983 | 14.2239 | 12.7695 | 16.507 | 15.3679 | 15.0433 | 16.9764 | 15.7483 | 15.1303 | 17.1288 | 17.1417 | 16.0263
Gas (incl. CHP) | 37.591 | 36.2529 | 37.9154 | 32.0463 | 26.7054 | 24.7651 | 22.5408 | 24.2522 | 26.7147 | 23.7024 | 20.9518 | 22.6636 | 21.3148 | 23.3316 | 28.6167 | 25.7372 | 23.1942 | 23.0202 | 26.0632 | 25.7269 | 33.5598 | 33.8675 | 32.0702 | 41.3386 | 36.4946
Coal | 33.3578 | 18.0886 | 18.1498 | 33.4102 | 39.9065 | 29.6341 | 27.3111 | 38.6699 | 39.3016 | 27.3576 | 25.1903 | 31.7263 | 32.7735 | 20.958 | 15.0779 | 26.2722 | 28.0354 | 15.1926 | 12.1724 | 16.5847 | 13.9376 | 4.3415 | 2.5808 | 8.2778 | 9.9763
Other fossil | 1.5104 | 1.211 | 1.4331 | 1.3144 | 1.5027 | 1.4167 | 1.325 | 1.5271 | 1.2572 | 1.2482 | 1.3166 | 1.2241 | 1.4173 | 1.3502 | 1.3019 | 1.3105 | 1.586 | 1.4573 | 1.5802 | 1.5282 | 1.5956 | 1.7081 | 1.6505 | 1.8804 | 2.0931
Wind | 3.1996 | 3.3977 | 2.8207 | 5.5431 | 4.7408 | 3.6985 | 4.1127 | 6.2531 | 6.4336 | 6.1751 | 4.5127 | 9.9306 | 10.5377 | 4.885 | 4.9023 | 10.1758 | 11.2882 | 7.9492 | 6.9011 | 12.3172 | 11.0187 | 6.9447 | 7.8266 | 9.8439 | 12.0596
Solar | 0.015217 | 0.065561 | 0.10476 | 0.056988 | 0.17796 | 0.43714 | 0.55318 | 0.18319 | 0.1397 | 0.69801 | 0.8547 | 0.30524 | 0.46498 | 1.4569 | 1.5441 | 0.54241 | 0.92779 | 3.078 | 2.673 | 0.78869 | 1.4496 | 3.8303 | 3.71 | 1.3195 | 1.6712
Other RES | 4.6374 | 4.2735 | 4.5558 | 5.437 | 5.7178 | 3.7742 | 4.5631 | 5.8531 | 5.3554 | 5.9945 | 5.1658 | 6.1313 | 6.7634 | 6.5208 | 6.647 | 8.3825 | 8.9004 | 8.3728 | 8.0078 | 9.961 | 10.4962 | 8.5265 | 7.2477 | 8.6849 | 10.2979
EDF Energy is the UK’s largest electricity generator
Chart: 
| EDF Energy | RWE UK | Centrica | SSE | E.ON | Drax | Scottish Power | Engie | Other
Column1 | 21 | 12 | 9 | 8 | 8 | 5 | 4 | 2 | 31
Source: All time (quarterly averages) – http://nationalgrid.stephenmorley.org/
Total 2016 output (TWh)
Notes: 2 – leave blank for now, I will need to find this chart

## Slide 9: The challenge: demand will increase as we lose capacity
Chart: 
| 2016 | 2016 capacity generating in 2035 | New build gas needed by 2035 | Low carbon needed by 2035
Blank | 106.9065 | 144.8547
Nuclear | 65.1491 | 8.1009
Gas (inc. CHP) | 140.8361 | 44.6141 | 37.9482
Other fossil | 35.9724 | 0
Wind and solar PV | 45.9433 | 36.8535 | 65.2585
Other RES | 34.9553 | 17.338 | 122.4538
Total | 322.8561 | 332.567
Electricity demand will increase because of population and economic growth and more electric vehicles, partly offset by energy efficiency
Source: EDF Energy analysis
NUCLEAR
GAS (INC. CHP)
OTHER RENEWABLES
WIND AND SOLAR PV
CLOSING
Ageing infrastructure will need to be replaced, large amounts of capacity will have closed between 2016 and 2035
  UK electricity demand forecast
  TWh/year
  Generation, TWh
  (after net imports and storage)
OTHER FOSSIL
  2016-2035 capacity closing
7 Nuclear stations (8GW)
32 gas stations (18GW)
13 coal + oil stations (20GW)
We need new low-carbon options if we are to achieve climate commitments (80% CO2 reduction by 2050)
Chart: 
| 2016 | Households | Economic activity | Energy efficiency | Electricity share | 2035
2016 | 308.7916 | 308.7916 | 329.738 | 318.4718 | 318.4718 | 339.2523
Households | 20.9464
Economic activity | 31.9928
-43 | 43.2589
Electricity share | 20.7805
Notes: RES means ‘Renewable Energy Sources’
‘Retirements by 2035’ means power stations / windfarms due to be closed down by 2035
These power stations need to be replaced with new gas stations (red bar showing 38), and new nuclear power stations or windfarms that don’t emit carbon dioxide

## Slide 10: The solution: investment needed across technologies
Chart: 
| 2016 capacity generating in 2035 | New build gas needed by 2035 | Low carbon needed by 2035
Blank | 106.9065 | 144.8547
Nuclear | 8.1009
Gas (inc. CHP) | 44.6141 | 37.9482
Other fossil | 0
Wind and solar PV | 36.8535 | 65.2585
Other RES | 17.338 | 122.4538
Total | 332.567
NUCLEAR
GAS (INC. CHP)
OTHER RENEWABLES
WIND AND SOLAR
OTHER FOSSIL
2/3 of low carbon needed through CfDs has yet to be procured
CfDs to date
Our analysis suggests that a mix with around one third gas, renewables and nuclear offers the best solution
26 TWh Nuclear
43 TWh Renewables
A significant amount of new low-carbon capacity needs to be built
Some of this has already been secured through Contracts for Difference (Hinkley Point C, offshore wind and biomass)
Much more low-carbon capacity still needs to be procured through CfDs
Investment in new gas also needs to be secured
The UK must find a solution that meets consumer requirements of reliable, affordable, low carbon electricity
This will require a mix of technologies, Government policies are designed to deliver the right mix for customers
  Generation, TWh
  (after net imports and storage)

## Slide 11: Gas can support a flexible low-carbon system – but is not low-carbon
Continue to support the development of flexible gas generation
25GW of new gas capacity needed, with a mix of highly efficient stations, and smaller flexible plants - equivalent to 20 large gas stations
If we want to hit our climate change targets, gas can’t contribute more than 1/3 to our energy mix in the 2030s
Not low carbon
Volatile prices
Relies on international import markets and infrastructure
Flexible
Relatively low capital cost
Will help balance renewables
NUCLEAR
Chart: 
GAS
WIND
SOLAR
  Gas prices are volatile
Source: EDF Trading
Notes: Some flexible gas capacity will help balance renewables in the generation mix
But its use will be limited because it is not low-carbon
By 2030s gas has to contribute at maximum ~1/3 of the energy mix (consistent with <100g/kWh) if we are to be on track to hit our climate change targets
Using gas also exposes consumers to volatile international gas prices and increasing reliance on imported gas

## Slide 12: Make use of UK wind resources – but there are limitations
Chart: 
GAS
WIND
SOLAR
NUCLEAR
Source: Map developed by 3Tier, www.3tier.com
The UK is well positioned to use wind resources
Support the development of new low-cost onshore and offshore wind, including on Scotland’s remote islands
The UK has the potential to deliver 14% of demand from its onshore wind resources
The cheapest wind power will come from onshore sites in Scotland where there is local support
Wind projects on remote Scottish islands offer good value for money and significant community and industrial benefits
Intermittent: wind farms on average only produce 30-45% of their potential power
Every new MW of capacity adds cost and complexity to managing the grid
Varying levels of public acceptability – more popular in Scotland where sites are best
A plentiful UK natural resource
Low carbon
Costs have fallen
Community support in Scotland and remote islands
6x less when not windy
GW
Windy week
Still week
1 week (hours)
Notes: ADD DATES
*****************************************
JD
Support RIW
Rethink onshore wind
Key point: you can’t build a reliable/affordable system on renewables alone – look at Denmark (attached to Sweden+Germany)
UK – Scotland in particular has one of the best wind resources in Europe
Onshore and remote island wind should be use to their full potential, plus best available offshore sites: but relying too heavily on renewables means costs will be higher
Above 20% penetration of intermittent generation, more and more of the energy is available at times when it isn’t needed: this pushes up the cost.

## Slide 13: Solar can provide too much in summer and too little in winter
Chart: 
Support solar installation to a manageable limit
Too much solar is adding cost and making the grid hard to manage
UK demand is highest on cold, dark winter nights – when there is no sun
Without metering and controllability solar deployment should be limited to 20GW.
Intermittent and highly seasonal
Not available when demand is highest
Adds cost and complexity to managing the grid
Low carbon – but higher CO2 footprint than wind or nuclear
Solar is already helping to provide daytime power in the summer months
Prices are falling
GAS
WIND
NUCLEAR
SOLAR
Solar output has great seasonal variability
Sunny summer week
Dull winter week
1 week (168 hours)
Source: Map developed by 3Tier, www.3tier.com
The UK is less ideally located for solar power

## Slide 14: Nuclear is reliable and low-carbon
GAS
SOLAR
NUCLEAR
WIND
Nuclear output is much more predictable
Nuclear’s always on power will be even more important in the future with more renewables and fewer fossil-fuelled power stations.
Any other low-carbon power mix that doesn’t use nuclear would cost consumers more
Large and small-scale nuclear power stations will support this mix, and a variety of technologies will provide further flexibility and choices for local communities
Large power stations support a stable grid frequency
Long construction time and high financing costs
Decommissioning/waste management costs (included in HPC CfD)
Not particularly flexible
Reliable power – will produce average of 91% of max capacity
Very long operating life
Low carbon
Cost competitive with other low carbon technologies
Majority of outages are planned
UK nuclear excellence
Last year the current UK nuclear fleet achieved its best output since 2003
Life extensions mean the fleet will operate well into 2020s
Two-thirds of outages are planned, and organised to minimise grid disruption
Chart: MW
BMRA Nuclear Generation data 2016
Notes: Nuclear is low carbon, reliable, will reduce costs for consumers in the long term vs other options; is being built now
Don’t forget SMRs
This is the key point of the pack – without a contribution from nuclear, any other option for a low-carbon energy system would cost consumers more.
You need to ensure that nuclear capacity is replaced if you want a reliable, affordable low-carbon energy mix.
The best value low-carbon energy system includes nuclear
Graph is fairly clear, but needs a bit of reading/explaining before the point is obvious. Could be re-arranged to show a rising trend of prices when using different technology mixes. The current graph is good at explain that super-cheap wind/solar PV on their own don’t equal a good value energy system to consumers.
Map of NNB sites and progress?

## Slide 15: Batteries can help manage these technologies but work best over short periods
Chart: 
| Day | Week | Month | Year
£60/MWh renewables with current storage cost (£400/kWh) (£) | 202 | 1056 | 4377 | 51862
£60/MWh renewables with cheaper storage (£100/kWh) (£) | 95 | 309 | 1139 | 13010
cheaper storage grey | 95 | 95 | 95 | 95
Source: EDF Energy analysis
GAS
SOLAR
NUCLEAR
WIND
  Costs of domestic storage
Battery storage is an emerging technology that has the potential to help stabilise the grid and store renewable power for a limited period of time
Market rules may need to change to help make the most of battery storage
Storing solar electricity in the day to use at night adds around £140/MWh to its cost, but this is expected to fall, and could reach £35/MWh
At today’s prices, it would cost £24 billion to build enough battery capacity to supply peak demand
The longer you store it the more expensive the power becomes
Cost is an addition to the cost of producing the electricity
Too expensive to store summer energy for use in the winter
Significant lifetime CO2 content from manufacturing
Already providing services to help keep the grid stable on a minute by minute basis
Costs are high but reducing
Could help store energy from renewables overnight
£60/MWh renewables with current storage cost (£400/kWh) (£)
£60/MWh renewables with cheaper storage (£100/kWh) (£)
Notes: £MWh – add label
Batteries will play a role, but they’re expensive and they can only viable on a minute by minute basis
For this – key point is that batteries are not expensive per se but ARE when they store over periods more than a day.
Energy storage is VERY expensive - currently only economically practical on an hourly basis.
Demonstrating the current and future costs of energy storage.
There is a perception that storage plus renewables is the holy grail – while forgetting what the cost is.
Storage plus renewables can deliver an affordable low-carbon energy system.
Review capacity market rules and network charges to ensure that the benefits of battery storage are awarded appropriately
Battery storage is currently very expensive, and only viable on a minute by minute basis.
The graph is pretty good, but could be simplified a bit. Simply language of text a bit, but overall content is good.

## Slide 16: An equal balance of nuclear, renewables and gas deliver’s Britain’s energy needs
NUCLEAR
WIND
GAS
SOLAR
Typical winter week
Typical summer week
GAS (INC. CHP)
OTHER RES
WIND
OTHER FOSSIL
CSS
SOLAR
PEAKING
STORAGE
NUCLEAR
Nuclear will be an important part of the future mix
A mixed system made up of roughly one third nuclear, renewables and gas will create a reliable, low-carbon system that is affordable
This makes the most out of our natural resources, while providing back-up power when we need it
There is room for new and developing technologies, such as batteries, increased interconnection and marine
Generation after net imports
Chart: 
Chart: 
DEMAND
Notes: Excludes interconnection flows – typical generation
after net imports

## Slide 17: Do we have the right policies in place to deliver this investment ?
All technologies have a role to play:
Investment is required in gas, renewables, and new nuclear
Allowing onshore wind in Scotland could lower costs
Future new nuclear projects will need to be cheaper
Carbon Price Floor
Supports switch from coal to gas, and investment across low-carbon technologies, including existing nuclear stations
Capacity Market
Has secured power demand for upcoming winters. Range of technologies supported, and is delivering battery storage
Contracts for Difference
Already bringing forward low-carbon investment, including construction of Hinkley Point C, while competitive pressure has already delivered significant falls in the price of low-carbon generation
EMR is working, allow it to continue
Carbon Price Floor
Capacity Market
Contracts for Difference

## Slide 18
Cost of renewables by date of procurement, £/MWh (2012 prices)
Hinkley Point C strike price in context
EMR and competition between technologies is delivering cheaper low-carbon electricity
In 2025 there will be c135TWh of renewables at £111/MWh average price, adding c£90 to a typical customer bill
HPC will represent 26TWh at £92.5/MWh, adding around £12 to a typical customer bill once operational
There will be a further cost to customers of wind / solar intermittency which represents around £10/customer
HPC is lower cost than >80% of renewable generation procured to date, and costs for future nuclear will have to fall
Chart: 
| 2002-2008 | 2010-2019 | 2014 | 2015 | 2016 | 2017
RO (85 TWh) | 108
FIT (8 TWh) | 175
CfD FIDER (22 TWh) | 130
Auction 1 (7 TWh) | 108
HPC (26 TWh) | 92.5
Auction 2 (14 TWh) | 64
Integration costs | 5 | 5 | 10 | 10 | 10
Integration costs
RO
85 TWh
FIT
8 TWh
FIDER
22 TWh
Auction 1
7 TWh
HPC
26 TWh
Auction 2
14 TWh
  Competition is driving down low-carbon costs
Notes: Excludes integration costs of £10/MWh for wind and solar PV. RO cost includes value of electricity sold based on historical prices 2012-2017; market forward prices 2018-2020 (as of Sept 2017) and BEIS UEP 2016 central prices 2021-2025.
Excludes large-scale hydro which is not qualify for renewable or low carbon support.
Integration costs for each procurement tranche are typically <£10/MWh as some generation is dispatchable biofuel rather than wind and solar PV.

## Slide 19: New nuclear programme making good progress
UK new nuclear
Significant construction progress at Hinkley Point C a year on from Final Investment Decision
Sizewell C stage 2 consultation completed
Design assessment has begun for UK-HPR1000 to be used at Bradwell
Flamanville 3, France
Testing regime has begun
Due to begin operation at the end of 2018
Taishan, China
Final testing of systems taking place
Unit one due to begin operation by the end of this year
Second unit due to follow in 2018
A year of progress at Hinkley Point C: 2,000 workers on site, 4 million m3 of earth moved, 10,000 tonnes of rock delivered for seawall, nuclear safety concrete poured for first permanent structures, construction of 500 meter jetty, onsite accommodation built, local road works complete

## Slide 20: EPR Nuclear Waste Summary
Waste management assumptions based on prudent and practical Government Base Case
  LLW minimised and disposed to LLWR or successor site
  ILW stored and disposed of to GDF during decommissioning
  Spent fuel stored and disposed of to GDF following further post decommissioning storage
Funded Decommissioning Programme to meet costs

## Slide 21: Funding Arrangements
Approved Funded Decommissioning Programme needed before construction of first structural concrete with nuclear safety significance
Will set out costs of waste management and decommissioning and arrangements for establishment of independent fund
Legally binding on operator – failure to meet obligations is a criminal offence
Costs of waste disposal derived from a contract with Government
Liability and funding for waste management and disposal expected to transfer to Government at end of reactor decommissioning

## Slide 22: Radiation and routes to human harm
Direct Radiation
    Alpha stopped by paper
    Beta stopped by aluminium sheet
    Gamma stopped by thick concrete / water
    Neutrons stopped by thick concrete / water
    Ingestion
      Particularly dangerous radionuclides once absorbed into the body
      Iodine 131 – beta radiation, concentrates in thyroid
      Caesium 134/137 – beta gamma radiation, concentrates in soil and food chains Strontium 90 – beta radiation, concentrates in bones
    But humans live with background radiation every day
      Average public dose – 2.7 millisieverts
      Average dose in Cornwall – 7.8 millisieverts
      Long haul flight – 40 – 60 microsievrts (1000 microsieverts = 1 millisievert)

## Slide 23: Annual outputs from a single UK EPR
12.5TWh* of electricity produced per year - enough electricity for approx 2.5m homes.
* 1 TWh = 1 billion kWh
30 Te (U) spent fuel produced****
Dose to most exposed Adult from Radioactivity discharged to air (0.004 mSv)**
Negligible CO2, NOX, SO2
73.15 m3 LLW generated***
9.35 m3 ILW produced***
Dose to most exposed adult from Radioactivity discharged to sea (0.017 mSv)**
All data is average per year
of operation.
Photo of EPR
** Dose data from GDA. PCER
Chapter 11: Radiological Impact
Assessment, Issue 1.
Note: Individual typical total dose in the UK varies between 2.3 to 7.3 mSv per year.
*** Waste volumes from GDA. PCER
Chapter 6: Discharge and Waste, Issue 02.
**** From GDA assessment:
1 fuel assembly = 527.5kg Uranium.
Total 3400 fuel assemblies/60 years.
Therefore, 57 SFA’s per year.
57 x 527.5 = 30067.5kg (1.5m3).

## Slide 24: Low Level Waste (LLW)
Comprises materials from routine operations with low levels of radioactive contamination.
Treated and disposed of through a variety of routes including the national LLW Repository (the LLWR) and commercial incinerators
A sub-set of LLW is categorised as Very Low Level Waste (VLLW) which may be suitable for alternative disposal or treatment routes.

## Slide 25: ILW Management
ILW generated from operation of nuclear power stations
Waste processed to meet RWMD requirements for a future GDF
ILW Transferred to on-site Interim Storage Facility
Disposal to future Geological Disposal Facility c.2080
Re-categorisation of ILW to LLW during storage
Notes: The proposed strategy for ILW conditioning and packaging at HPC is that operational ILW would be conditioned and treated using the same procedures as applied during the operation of existing PWRs in France with due consideration for UK specific requirements.
Utilisation of C1 and C4 concrete packages.
Cementation for all waste except ion exchange resins which will be processed using Mecure machine (polymer solidification process).
LOC: Before conditioning and packaging of ILW, regulatory arrangements require that sites produce an ILW conditioning proposal. This would include a demonstration that, following conditioning, the waste would be compatible with existing or future planned management and disposal options. This requires that a Letter of Compliance (LoC) is obtained for the packaging proposal. The LoC process is the mechanism that the NDA Radioactive Waste Management Directorate (RWMD) utilises to provide confidence that a waste package can be accepted at a future GDF.
Decay Storage – Due to the long period of interim storage the radioactivity of a proportion of the ILW that would be generated during operation of the HPC UK EPRs (dominated at the time of arising by relatively short lived radionuclides including cobalt-60 (half life of 5.27 years), caesium-137 (half life of 30.2 years) and iron-55 (half-life of 2.7 years)) would have reduced to such levels that the waste would no longer be classified as ILW. This waste would therefore be managed as LLW.
Geological Disposal Facility – assumed that it will be ready to accept ILW from Hinkley Point C in 2080 - after the end of electricity generation.

## Slide 26: Spent Fuel Management
Initial Cooling in reactor pond
EPR design has limited reactor storage
Government base case assumes on-site storage of spent fuel
Need to develop additional on site spent fuel storage facility to take lifetime arisings
Chooz B1, (1,500 MWe) Fuel Building

## Slide 27: Spent Fuel Packaging
Current NDA repository assumptions based on Swedish model
Requires packaging of spent fuel in copper sheathed canister
Suitable for repository in hard or soft rock – but site and geology yet to be agreed
Conservative cost assumptions included in Funded Decommissioning Programme

## Slide 28: Hinkley Point C – Spent Fuel Management
Spent Fuel generated from operation of nuclear power stations
Spent Fuel Transferred to Reactor Pool (storage for up to 10 years)
Spent Fuel Transferred to on-site Spent Fuel Interim Storage Facility (stored for up to 50 yrs after End of Generation)
Disposal to future Geological Disposal Facility c.2130
Spent Fuel Transferred to Encapsulation Facility
UK PROTECT – COMMERCIAL in CONFIDENCE